## Slide 1: Managed Automaton - SESP
Greg Chasteen

## Slide 2: Agenda
  Brief discussion on Insight, SEEC
  Focus on SESP provided APIs
  Detailed look at some of the more popular individual APIs
  How to combine into common worklfows
  Sample SESP open and save utility

## Slide 3: Working With PDM Managed Documents
Each Solid Edge PDM client provides an API
  Insight
    Will provide documention
  Solid Edge Embedded Client ( SEEC)
    Will provide documentation and examples
  Solid Edge for Sharepoint (SESP)
    Will provide documented examples

## Slide 4: Insight API’s
All Solid Edge API commands are “INSIGHT” enabled
  File Open (both interactive command and API) accepts either url or folder based name, cache, etc.
  Revision Manager.Open will automatically check-out a file managed by Insight.
There is an INSIGHT automation layer to directly access/execute INSIGHT server specific commands such as download/upload/check-in/check-out etc.
Insight API’s available on both Revision Manager and Solid Edge Framework object models

## Slide 5: Insight API’s
Let’s take a quick look at the Insight API’s using Object Browser

## Slide 6: Insight API’s
Document containing details on each API
  USB drive provided
    Advanced Track\Reference Material\InsightExamples.doc
  TIP
DisplayAlert will suppress all authentication dialogs as well as the Edit Profile dialog.

## Slide 7: SESP and SEEC APIs
Very similar design. In fact, whenever possible an exact duplicate
Access to APIs via SolidEdgeFramework type library
  SEEC – SolidEdgeTCE
  SESP – SolidEdgeInsightXT
Let’s take a look at them via object browser

## Slide 8: SESP and SEEC APIs…. Some differences
ValidateLogin
Purpose: This API is used to authenticate the user before calling any others SEEC functions.
Syntax: Call ObjSEEC.ValidateLogin( UserName, Password, Group, Role,URL)
Parameters:
  UserName (Input): Specifies the UserName of the user to authenticate
  Password (Input): Specifies the password of the user to authenticate
  Group (Input): Specifies the group to which the user belongs. The default group is “dba”
  Url (Input) : Specifies the TC database. Can be 2 Tier or 4 Tier
Note: The behavior of the authentication process depends on the display_alerts flag. If the value of the flag is OFF, then Validatelogin () method internally silently (i.e. without showing any Login dialog) does Auto login using supplied credentials.

## Slide 9: Example logging into SEEC

## Slide 10: SESP and SEEC APIs…. Some differences
API Name: ValidateLogin
Purpose: This API is used to login into SE SP.
Note:
The API actually uses to log in to the SE SP.
The behavior of the authentication process does NOT depend on the display_alerts flag.
Establishes the connection to the Sharepoint database!

## Slide 11: SESP API’s
Notice there was not an Open API…
Slightly different approach than the Insight API’s with regards to C-O\Open, C-I\Close
  The Documents.Open API does not take input directly from the SESP database
    The document must downloaded to the SESP cache
      At this point the Documents.Open from the SESP cache

## Slide 12: SESP API’s
Create a new document and save to the database
  Create the new Solid Edge document
  Prep the document with the necessary information
    Part number
    Revision
    Folder location
    Content type
  Import the prepped document with the ImportDocumentsToServer API

## Slide 13: SESP API’s
Lets look at some common SESP API workflows in detail
You can follow along….
AdvancedTrack\_06-ManagedAutomation-SESP\Programs\SESP-AutomationSamples.sln

## Slide 14: More examples
Utility that uses SE SP APIs along with some Sharepoint APIs.
AdvancedTrack\_06-ManagedAutomation-SESP\Programs\InsightXTSPTools

## Slide 15
Greg Chasteen Solid Edge Technical Acct. Manager Solid Edge Development
675 Discovery Drive Suite 100 Huntsville, Al 35806
Phone: +1 (256) 705 - 2621 Mobile: +1 (256) 479 - 9055 E-mail: chasteen.gregory@siemens.com